## Slide 1: Workshop in Software Models
Delivery Drone Project
Guy Haviv
Noa Davidovitch

## Slide 2: Spectra Requirements
Full functioning Delivery Drone based on variables, guarantees and assumptions which are declared and synthesized using Spectra language.
  Maintain a request & delivery drone system between houses and warehouse
  Every request must be picked up eventually
  Every request picked up, must be delivered to its destination eventually
  Each location holds only one request before pickup – the last one sent
  Request & wait mechanism for packages & envelopes to be picked up
  Default Drone inventory includes room for 6 envelopes and 2 packages
  Drone must drop off package/envelope when it can
  Changing movement policy with regards to winds
  Changing pickup policy with regards priority packages from the warehouse
  Managing pickups with a limited battery

## Slide 3: GUI Requirements
GUI representation of the Spectra controller’s system simulation
  GUI displaying all Spectra components in the specification
    Houses, warehouse, charging station etc.
  Responsive GUI - updates in accordance with the controller’s system responses
  Clear and meaningful visual representation for each component and the system’s state
  Easy UI menu components:
    Adding requests (controlling environment variables)
    Switching modes (manual / automatic)
    Executing pre-defined scenarios

## Slide 4: Spectra Specification –Basic Environment & Basic Assumptions
Basic environment include 3 boolean arrays:
  outHousePackages[i]- represent new request from house #(i+1) to the warehouse.
  outWarehousePackages[i]- represent new request from warehouse to house #(i+1)
  envelopeRequests[i]- represent if the request from house #(i+1) is an envelope.
Basic assumptions:
  At initial state:
    No requests from houses.
    No requests from warehouse.
    All envelope requests are off.

## Slide 5: Spectra Specification – System & Monitors
3 system variables:
  Drone - array of 2 Cord to represent the drone location on the grid.
  PickUpThisState - number between 0 to 8 – represent current pickup by location.
  DropOffThisState - number between 0 to 6 – represent current drop-off by location.
8 monitors:
  Each house has 2 monitors:
    Monitor to remember a request from house to warehouse
    Monitor to remember a request from warehouse to house
  Example:

## Slide 6: Spectra Specification – Defines
Locations – atWarehouse, atHouse#, atChargingStation
  Coordinates on the grid of those locations.
  The locations can be changed.
Capacity – PACKAGE_CAPACITY, ENVELOPE_CAPACITY
  Maximum packages/envelopes the drone can held in his inventory.
  All capacities are parameterized and can be changed.
Pickup – housePickedup, warehousePickedup, housePackagePickup
  true if the drone is picking up request from house/warehouse.
Delivered – packageDelivered, envelopeDelivered
  true if the drone is dropping off package/envelope.
Room for pickup- roomForPickupPackage, roomForPickupEnvelope
  true if the drone inventory is not full.

## Slide 7: Spectra Specification – Basic Counters (Inventory system)
7 counters:
  4 counters (one for each house): count packages on the drone for each house destination.
  2 counters : count how many packages/envelopes on the drone are destined to warehouse.
  1 counter : count total number of packages on the drone.
Examples:

## Slide 8: Spectra Specification – Guarantees (drone movement & pick-up mechanism)
Drone movement:
  Drone can move up to one step both row and column directions.
  Base on the predicates:
Pick up mechanism:
  Use pattern pResponseToS - every waiting request must be picked up eventually.
  Pick up can be made only if there is room on the drone, the drone at location,
  and there is a waiting request.

## Slide 9: Spectra Specification – Guarantees (drop-off mechanism)
Drop off mechanism:
  Use pattern pResponseToS - if the drone has package/envelope to specific location, it eventually be there.
  Drop off iff the drone is at the location and its capacity to this location is not empty.
  If drone has package/envelope to specific location and it is in the same location, it will not move until drop off.

## Slide 10: Spectra Specification – Priority Mode
Environment & assumption:
  priorityMode initialized to false
  When true - warehouse packages are prioritized for pick-up over house requests.
    Drone can pick up only up to priorityCap # of packages before a warehouse package.
1 counter:
  Counts how many house packages were picked up while in priority mode, up to priorityCap.
1 guarantee:
  By default, only one request can be picked up before priority request.

## Slide 11: Spectra Specification – Winds Mode
Environment & assumption:
  windsMode initialized to false
  When true - the drone can only move sideways )not diagonally(.
1 guarantee:
  Drone moves both coordinates (including diagonally) means no winds are on.

## Slide 12: Spectra Specification – Energy
Define how many packages the drone can pick up before his battery empties.
1 counter:
  Counts how many packages were picked up since the last visit in the charging station.
1 guarantee:
  Battery should never be empty.
Notice: envelopes are light, as such, they do not count against the energy counter.

## Slide 13: Spectra Variants
Native Variants:
  There are three modulable features that can be “turned off” at the specidication files.
    Winds, Priority, Energy.
  In the specification files there are comments regarding which line should be commented out in order to turn off each feature, independently.
Extra Variants:
  Charge when needed: drone can not go to charging station before picking up at least X packages (X is parameters).
  Must pick up: drone can not leave a location if it has a waiting request.
    This specification variant uses only basic features (i.e no winds, priority nor energy).
  No ‘must drop off’: canceling the drone requirement for a drop-off when eligible (at location, with a package to drop off)
  Triggers:
    add use of triggers to the specification
      If charging (and did not come from warehouse) - pass by the warehouse.
      "House visit fairness" - If at a house, after 2 "safety" states (for pickup/drop-off) , do not visit the same house for at least 5 states.
Unrealizable:
  Must pick up without considering cases which the drone cannot make a pick up
    Such as when priority mode is true and can not pick up any more requests from houses (priorityCap is maxed).

## Slide 14: Simulation – Main Screen
Built of 3 main components:
  Main Grid
    Houses
      Waiting deliveries on the left
      Dropped deliveries on the right
    Warehouse Board
      Shows waiting deliveries
    Charging station
    Drone – moving between locations
  Control Panel
  Menus

## Slide 15: Simulation – Control Panel
Priority
  Indicator if mode is ON/OFF
  Current capacity of the priority cap
Stocking - Reflects if the drone picks up / drops off a package in this state
Battery – indicates drone’s remaining energy
Inventory
  Current capacity of the drone’s inventory – both for packages and envelopes
  For packages – shows distribution by destination

## Slide 16: Simulation - Menus
Manual Menu
  Add requests
    Select source (toggle button)
    Select type and destination from the dropdown menu
    Click “Add request”
  You can also just “Randomize a request” for a quick add
  Toggle Modes – both visually and as an environment variable
    Winds Mode
    Priority Mode

## Slide 17: Simulation - Menus
Scenario / Auto Menu
  Run Demo – start automized environment
  Run Scenario – choose a scenario from the dropdown list, each one has a tooltip with the scenario description
    Fast forward step button – when running a scenario, you can speed up the simulation to run fast through a step.

## Slide 18: Simulation – Configuration Screen
Optional UI solution for enabling modulization of the specification advanced features
At startup, simply select which features are enabled in your specification file – the GUI will adjust accordingly

## Slide 19: Pre-defined Scenarios
Scenario No. | # of Steps | Description | Comments
1 | 2 | A package is sent from the warehouse to a random house | Most basic drone operation
2 | 1 | All houses request a package or an envelope delivery | Check enforcement of drone’s inventory system - with default capacity of 2 packages.
3 | 1 | Priority mode, with no warehouse packages | Priority Mode is nullified when warehouse is empty
4 | 1 | Pickup only: 3 warehouse packages, 2 house envelopes - with Priority Mode | Testing priority mode behavior
5 | 5 | Pickup only: all houses request package delivery, with a 4-package refill after a pickup. Partial use of Winds Mode | Keeping houses requests full longer, test winds mode behavior

## Slide 20: Pre-defined Scenarios
Scenario No. | # of Steps | Description | Comments
6 | 1 | Full Delivery of Full Grid, - All houses request delivery, warehouse full as well. With Winds Mode | Busiest scenario
7 | 5 | Full Delivery: Carousel of house packages - Requests coming in cycle (1,2,4,3) | Interesting when inventory capacity allows pickup for all packages
8 | 2 | On-the-way Pickup: Random WH request to a house, upon pickup - add delivery request from that house. Full Delivery of house request. | Check if the drone will pickup a waiting package where he makes a drop-off